## Slide 1
Formulation & Process Engineering of Paracetamol 500 mg Immediate-Release Tablets
Wet Granulation Optimization, Excipient Compatibility, and In-Vitro Dissolution Profiling
Case Study: Industrial Formulation Design
Paracetamol 500 mg IR Tablet | Slide 1
Notes: Speaker Notes:
This presentation explains the formulation strategy and manufacturing process for Paracetamol 500 mg immediate-release tablets using wet granulation to improve flow, compressibility, and tablet robustness.

## Slide 2
API Physicochemical Profiling
Chemical name: N-(4-hydroxyphenyl)acetamide
Molecular weight: 151.16 g/mol
BCS: commonly described as highly soluble with permeability-dependent classification; verify the exact regulatory classification for the target jurisdiction
Key formulation challenges: poor flow, limited plasticity, elastic recovery and risk of capping
Wet granulation helps produce agglomerates with improved flow and compressibility
Paracetamol 500 mg IR Tablet | Slide 2
Notes: Speaker Notes:
Paracetamol can present tableting challenges, particularly in direct compression. Wet granulation is selected here to improve powder handling and tablet mechanical properties.

## Slide 3
Excipient Selection & Functionality Matrix
Paracetamol API — Active ingredient — ~75.0%
Microcrystalline cellulose PH-101 — Diluent/dry binder — ~12.0%
Pregelatinized starch (Starch 1500) — Binder/disintegrant — ~7.0%
Sodium starch glycolate — Superdisintegrant — ~3.5%
PVP K-30 — Granulating binder — ~1.5%
Magnesium stearate — Lubricant — ~0.5%
Colloidal silicon dioxide — Glidant — ~0.5%
Note: quantities are an illustrative development formula and must be confirmed by formulation trials and product-specific specifications.
Paracetamol 500 mg IR Tablet | Slide 3
Notes: Speaker Notes:
Each excipient is selected to address a specific manufacturing or performance need. The formula should be optimized experimentally for tablet strength, disintegration and dissolution.

## Slide 4
Wet Granulation: Manufacturing Unit Operations
1. Sifting: API and intragranular excipients through 40-mesh (~425 µm)
2. Dry mixing: Rapid Mixer Granulator for about 10 min
3. Wet massing: add aqueous PVP K-30 solution to the required granulation endpoint
4. Drying: Fluid Bed Dryer at about 55 ± 5°C; target LOD 1.0–1.5% as a development target
5. Sizing: pass dried granules through 20-mesh
6. Final blending/lubrication: add extragranular excipients and magnesium stearate
7. Compression: rotary tablet press with suitable tooling
Paracetamol 500 mg IR Tablet | Slide 4
Notes: Speaker Notes:
The critical step is endpoint-controlled granulation. Drying and sizing must produce granules with suitable moisture, particle-size distribution and flow before compression.

## Slide 5
In-Process Quality Controls & Dissolution
In-process controls:
• Tablet weight and weight variation
• Thickness and hardness: development target 6–9 kp
• Friability: development target <0.5%; pharmacopeial acceptance commonly NMT 1.0% for conventional tablets
• Disintegration: development target <5 min
Dissolution development setup:
• USP Apparatus II (Paddle), 50 rpm
• 900 mL medium; pH 5.8 phosphate buffer or 0.1 N HCl depending on validated method
• 37 ± 0.5°C
• Acceptance criterion must follow the applicable pharmacopoeial monograph/validated specification; do not assume Q = 80% in 30 min without verification
Paracetamol 500 mg IR Tablet | Slide 5
Notes: Speaker Notes:
Quality testing should use validated, product-specific methods. The dissolution specification should be taken from the applicable pharmacopoeia or approved product specification.

## Slide 6
CQAs & Troubleshooting
Critical Quality Attributes (CQAs): assay/content uniformity, tablet weight, hardness, friability, disintegration, dissolution, moisture and appearance
Capping/lamination — possible causes: air entrapment, excessive compression speed, elastic recovery or unsuitable granule moisture
Corrective actions: optimize granulation endpoint/moisture, compression speed, dwell time and binder level
Dissolution lag — possible cause: excessive magnesium stearate or over-lubrication
Corrective action: minimize lubricant level and blending time while maintaining ejection performance
Process control principle: link material attributes + process parameters → CQAs → finished-product performance
Paracetamol 500 mg IR Tablet | Slide 6
Notes: Speaker Notes:
Troubleshooting should begin with identifying the material or process variable responsible. Changes should be evaluated through controlled development trials rather than using a fixed correction universally.